## Slide 1
Planck’s constant in the light of an incandescent lamp

## Slide 2
Introduction

## Slide 3
The idea of light quanta
Planck (1900): emission of radiant energy by matter does not take place continuously, but in finite “quanta of energy” h (h= Planck’s constant 6.63x10-34 J.s,  =frequency)
Einstein (1905): light quanta (photons) as inherent in the nature of radiation itself

## Slide 4
Distribution of intensity of heat radiation as a function of the wavelength
 :
Emissivity (=1 for perfect black-body radiation)
C1, C2 :
Constant parameters

## Slide 5
Where c2=hc/k
h: Planck’s constant
c: velocity of light
k: Boltzmann’s constant
Planck’s radiation law Radiation energy per time unit for the wavelength 
Main objective of this experiment

## Slide 6
Report on the experiment

## Slide 7
Emission of a 12 V tungsten lamp
u
wavelength, 

## Slide 8
The light spectrum emitted by the filament is continuous.
u
wavelength, 

## Slide 9
u
wavelength, 
Liquid filter
0
A narrow band of the visible spectrum is selected with a combination of Orange II and Copper Sulphate solution (it absorbs infrared strongly).

## Slide 10
We will assume that the selected band is nearly monochromatic.
u
wavelength, 
Liquid filter
0

## Slide 11
The wavelength of the selected band is in the spectral response range of a Light Dependent Resistor (LDR)
Liquid filter
0
u
wavelength, 

## Slide 12
From the formula:
For small 
Resistance R of LDR
is related to illumination as:
lllumination E on the LDR is
proportional to the transmitted energy
b: constant
 : parameter
Taking logarithms
Combining (2), (3) and (4):
Plotting
lnRldr
1/ T
Block diagram

## Slide 13
Experimental setup

## Slide 14
GENERAL DIAGRAM
Voltmeter
Lamp
Ammeter
Potentiometer
Battery
Solution filter
LDR
Ohmeter

V
A

## Slide 15
COMPONENTS
Platform
Potentiometer
Battery
Lamp
A
V

LDR
Cover
Ruler
Solution filter
Holder
Grey filter
Voltmeter
Ammeter
Ohmeter

## Slide 16
INSTALLING
THE
EQUIPMENT

## Slide 17
1
Turn the potentiometer knob anticlockwise up to the limit

## Slide 18
2
Turn slowly the tube holder aligning the lateral holes between the lamp and the LDR.

## Slide 19
Move the LDR towards its lateral hole, positioning its surface as the figure shows.
3

## Slide 20
Insert the solution filter tube in its holder.
4

## Slide 21
Put the cover onto the platform to protect from the outside light.
In order to ensure the correct initial conditions, LDR should keep in total darkness for at least 10 minutes before the measurements.
5

## Slide 22
Procedure
Some previous measurements are needed before using Equation (6)
T
0
R


## Slide 23
RB0 can be extrapolated to I = 0 from measurements of V and I,
V
A
Relation between the resistance of the filament (RB) and its temperature (T)
a can be derived from the filament resistance (RB0) at room temperature (T0)
Using the multimeter as a thermometer.
I
R
R0
T Temperature of the emmitting filament
RB
RB0
Experimental data fit

## Slide 24
 transmission of the filter
Solution of:
Orange II.
CuSO4 (it absorbs the infrared light).
0 = 590 nm
/nm

## Slide 25
 Parameter of the LDR
En
Rn
0.512En
Rn’
Grey filter

## Slide 26
R
V
A
COLLECTING DATA
V
I
R
RB=V/I
T = aRB0.83
RB-0.83
lnR
RB-0.83
lnR
V1
I1
R1
RB1
T1
RB1-0.83
lnR1
V2
I2
R2
RB2
T2
RB2-0.83
lnR2
V3
I3
R3
RB3
T3
RB3-0.83
lnR3
Vn
In
Rn
RBn
Tn
RBn-0.83
lnRn

## Slide 27
RB-0.83
lnR
From the slope
We obtain
And finally the Planck´s constant:
h: Planck´s constant.
k: Boltzmann´s constant.
c: speed of light.

## Slide 28
End of presentation